## Slide 1: Sonar Propagation Modeling using Hybrid Gaussian Beams in Spherical/Time Coordinates
Sean M. Reilly
University of Rhode Island, Ocean Engineering Department
and Alion Science and Technology Corporation
This paper defines a new undersea acoustic transmission loss model that is optimized for real-time, sonar simulation/stimulation systems in littoral environments. The ray solutions to the eikonal equation are computed in latitude, longitude, and altitude coordinates to match wide-area environmental databases. Hybrid Gaussian beam techniques for transmission loss calculation are used to extend the applicability of ray theory to lower frequency regimes. Numerical integration of the wave equation is performed in the time dimension to support broadband signal modeling. This 3-D approach also supports out-of-plane reflection from the ocean bottom. This paper derives the eikonal solution from first principles to ensure a complete understanding of the coordinate system’s impact.
162nd Meeting of the Acoustical Society of America
San Diego, California, 31 October - 4 November 2011

## Slide 2: Acknowledgements
This paper was developed as part of Sean Reilly’s PhD studies at the Ocean Engineering Department of the University of Rhode Island, under the direction of Dr. Gopu Potty and Dr. James Miller.
Parts of this effort have also been funded by the High Fidelity Active Sonar Training (HiFAST) Project at the U.S. Office of Naval Research, and internal research and development (IRaD) efforts at Alion Science and Technology, Inc.
The equations for reflection from a 3–D slope were developed by Dr. Michael Goodrich (Alion), who also made significant contributions to the development of test cases for this model.

## Slide 3: Key References
M. A. Pedersen, D. F. Gordon, Normal-Mode and Ray Theory Applied to Underwater Acoustic conditions of Extreme Downward Refraction, J. Acoust. Soc. Amer. 51 (1972) 323.
V. Cerveny, M. M. Popov, and I. Psencik, Computation of wave fields in inhomogeneous media - Gaussian beam approach, Geophys. J. R. Astron. Soc. 70 (1982) 109.
R.M. Jones, J.P. Riley, T.M. Georges, HARPO: A Versatile Three-Dimensional Hamiltonian Ray-Tracing Program for Acoustics Waves in an Ocean with Irregular Bottom, National Oceanic and Atmospheric Administration (NOAA) Report, (1986).
M. B. Porter, H. P. Bucker, Gaussian beam tracing for computing ocean acoustic fields, J. Acoust. Soc. Amer. 93 (1987) 1349.
H. Weinberg, R. E. Keenan, Gaussian ray bundles for modeling high-frequency propagation loss under shallow-water conditions, J. Acoust. Soc. Amer. 100 (1996) 1421.
P. A. Baxley, H. Bucker, M. B. Porter, Comparison of Beam Tracing Algorithms, Proceedings of the Fifth European Conference on Underwater Acoustics (ECUA) 2000.

## Slide 4: Research Objectives
Create a much faster TL model for real-time, littoral, active sonar sim/stims by revisiting fundamental assumptions of ray theory and Gaussian beams.
Speed goals:
  100 targets for one sensor
  Update rates faster than the speed of sound
  On a single core of an average laptop
Insignificant loss in accuracy at active sonar frequencies.
Once we have a fast algorithm, expand to additional sensors using better hardware (including GPUs).

## Slide 5: Technical Approach
3-D ray solutions are computed in lat, long, alt.
  Ray theory is expected to work best at frequencies > 1000 Hz.
  Supports out-of-plane effects in littoral environments.
  Improves speed by avoiding translation of environmental data into 2-DxN radials.
Time domain ray trace
  Improves speed by maintaining phase continuity of wavefront.
Hybrid Gaussian Beam techniques for transmission loss calculation (like GRAB).
  To improve accuracy in shadow zones and < 1000 Hz.
C++ implementation with a test driven development process.
  Only a few representative samples shown in slides that follow.

## Slide 6: Ray Tracing in Time Domain
1) derive eikonal
2) characteristic wavefronts using rays
3) define
4) convert
Coupled vector ODEs in 3-D
Solved using initial conditions & marching solution
this model
typical eikonal solution

## Slide 7: Ray Tracing in Spherical/Time Coordinates
latitude
= p/2-q
altitude = h
r = R + h
R
equator
Earth’s axis
center of
the earth
center of
curvature
area of operations
longitude = f
use WGS-84 ellipsoid, but assume uniform curvature over area of operations

## Slide 8: Adams-Bashforth 3 (AB3) Propagator
Estimates next time step from explicit terms in previous three.
  Implement as a cached circular queue of 4 wavefronts (trades memory for speed).
  Single calculation of sound speed and derivative (slowest calculations) per iteration.
  Single calculation of the slow sinq and cotq operations per iteration.
AB3 is as accurate and much faster than Runge-Kutta 3, but not self starting.
ti+1
ti
ti-1
ti-2
ti+2
wavefronts

## Slide 9: 3-D Ray Trace Testing
Time step
10 msec
100 msec (1:50)
Vertical OK? Munk Profile
At 130 km range, max deviation of 8.6 m with 100 msec and 0.25 m with 25 msec time step.
Path type
rhumb lines
model
Horz OK?  Great Circle Routes
Max deviation from great circle bearing is 2.81x10-10 degrees over 1500 km distance.
100 msec time step

## Slide 10: Ray Reflection from 3-D Slope
= surface normal at reflection point
= incident ray direction
= reflected ray direction
= component of incident ⊥ to normal
= time delay until reflection
Computing time of impact
Computing reflection direction
2nd order Taylor series propagator used to improve accuracy of incident ray direction during reflection
r
s
A
A
R
I
“wrong side of interface”
next
current
Notes: Double check the picture

## Slide 11: Reflection Testing
Vertical OK?  Analytic Slope
Horz OK?  Malta Escarpment ETOPO2
Ray D/E increases by twice the slope
to within 10-5 deg maximum deviation.
Reflection from realistic bottom
causes out of plane paths.
top view
50 msec time step
side view
1 msec time step
to measure angles
downslope
18 nmi offset
Bounces
bottom
surface

## Slide 12: Eigenrays: Wavefront Interpolation near Targets
Taylor series on d2 derivative
Neighboring Gaussian beams reuse r  speed benefit of time-domain ray tracing
t = travel time, m = launch D/E angle, j = launch AZ angle
d = distance from target to wavefront point
r = offset vector from CPA in time, D/E, AZ
g = gradient of squared distance at CPA, and
H = Hessian matrix of squared distance at CPA.
Side view
2

## Slide 13: Hybrid Gaussian Beam TL
Use spreading to estimate divergence instead of dynamic ray equations (like GRAB).
Mostly to avoid normalization problems reported by Baxley, Bucker, & Porter.
Form 2-D Gaussian beams that are centered between rays to make width calculation easier.
Re-use GRAB min-width factor, but re-cast as natural width + wavenumber windowing convolution.
Single eigenray collision used for all Gaussian beams. Time domain approach  contributions in phase.
Gaussian
beam centers
eigenray
target

j+1

j



k

j+2

j
-
1



k+1



k+2



k
-
1
2w
j+1
View across wavefront

## Slide 14: TL at Edge of Shadow Zone OK?
Source Depth = 66.7 yds
Receiver Depth = 66.7 yds
Frequency = 2000 Hz
c0 = 1677.3319 yd/sec
g0 = 1.2286762 1/sec
ref: M. A. Pedersen, D. F. Gordon, "Normal-Mode and Ray Theory Applied to Underwater Acoustic conditions of Extreme Downward Refraction", J. Acoust. Soc. Am. 51 (1B), 323-368 (June 1972).
Pedersen/Gordon N2 Linear Shallow Source Test Case

## Slide 15: Execution Speed OK?
Whole Mediterranean 30N-46N, 8W-37E
ETOPO2 bathymetry (2-D PCHIP interp)
WOA05 SVPs for Dec (PCHIP+Bi-Linear)
Dell Latitude D630 laptop
Sensor at 36N 16E
N random targets within ± 30 mins
181x25 ray paths, 100 msec time step
60 second propagation time
≈ 54% SVP
Interpolation
≈ 19% Bathy Interp
Speed Goal
Targets Memory
0 8 Mb
50 15 Mb
100 22 Mb
≈ 27% Rays + TL

## Slide 16: Conclusions
Positive comparisons to TL benchmarks  so far
  Strongly suggests that the theory derivation is OK.
Meeting original speed goals
  But  hypothesis of greatly improved speed over current models is still un-proven.
Room for even more speed improvements.
  Especially in SVP and bathymetry interpolation.